## Slide 1
Faculty of Engineering
ENGG1000 Engineering Design and Innovation
Semester 1 2018
Week 03:
Engineering Design Process
Problem Definition
Dr. Ang Liu
Email: ang.liu@unsw.edu.au

## Slide 2: What is this？
Use the verb to define the problem an artifact is intended to solve !

## Slide 3: Define an engineering design problem
Given the customer need of “cure cancer”
It can be formulated as a biological problem
  Design an experiment to understand how cancer is developed
It can be formulated as a pharmaceutical problem
  Design a new drug to detain the cancer development
It can be formulated as a policy making problem
  Design an insurance policy to reduce the cost of treatment
It can be formulated as an engineering problem
  Design a scanning machine to identify, image stage-1 cancers
  Design a big-data platform to analyse risk of developing cancer
  Design a medical device to remove cancer completely

## Slide 4: Values of problem definition
Design a MP3 player?
  Storage capacity
  Upload speed
  Sound quality
  Size and weight
  Battery life
Carry 1,000 songs in pocket?
  Where to find and download 1,000 songs?
  How to organize the 1,000 songs?
  How to pay for the 1,000 songs

## Slide 5
Good problem definition leads to innovation
Adjust towards the most
comfortable position
The floating keyboard
Repeated Stress Injury
Interrupt repetition of
the same position

## Slide 6: The Design Process
Formulating the problem to identify aspects of the task to be investigated.
Produce a problem statement.
Generate a range of design concepts for solving the problem
Critique and evaluate the proposed concepts.
Select the best solution
Evaluation of the Design
Concept Generation
Problem Definition
Detailed design and refinement.
Implementation – building and testing.

## Slide 7
Dym’s Model
From the definition:
…. stated
objectives … and
constraints.
Systematic …
generation then
evaluation ….
Client’s Problem Statement
Problem Definition
Conceptual Design
Preliminary Design
Detailed Design
Design Communication
Documentation for Final Design

## Slide 8
Translate the Client’s problem statement into
your problem definition.
Remember:
A bad problem statement will limit your choices in finding a good solution.
To that end, we need solution-independence.
Client’s Problem Statement
Problem Definition
Conceptual Design
Preliminary Design
Detailed Design
Design Communication
Documentation for Final Design
Problem definition is important for the assessments of problem definition, design proposal and design presentation.

## Slide 9
Elucidating the Design Problem:
From the Client’s Request through to the Generation of Concepts

## Slide 10
OBJECTIVES
Client’s Request
Problem Statement
Phase 1:
Problem
Definition
Objective
Tree
PCC
Constraints
Establish
METRICS
“Short List” of Concepts
Phase 1: problem definition

## Slide 11: Phase 1: problem definition
Dym’s four parts:
1.1 Clarify Objectives
1.2 Establish Metrics for Objectives
1.3 Identify Constraints
1.4 Revise the Client’s Problem Statement
Then…..
1.5 Identify the Functions and Requirements
 Articulate the Problem Definition in Engineering terms. But not today!

## Slide 12: 1.1 Clarify the design objectives
Gathering information is the key:
Target customers vs relevant stakeholders
Customer voices: surveys, focus groups, formal interviews, etc.
Lead users in the field
The Objective Tree may be a useful tool for you.

## Slide 13: An Example from Dym - “Design a Safe Ladder”
An “Objective Tree” (Dym, Figure 4.1), representing goals for our Device.
Remember that we need solution-independence

## Slide 14: Who are the real customers?

## Slide 15: 1.2 Establish a set of metrics
“First and foremost, a metric should actually measure the objective that the design is supposed to meet.”
– Dym
Decide what to measure, with respect to the objectives.
Determine the appropriate units (generic categories can be okay).
Make sure the metrics are repeatable and their value unambiguous.
The metrics, like the Objectives must be solution-independent.

## Slide 16: A Pairwise Comparison Chart as a tool for Prioritising Objectives For the ladder example from Dym:
A “PCC” (Dym, Table 4.4), ranking the importance of the goals for our Device.
Each objective should come from a common node on the Objective Tree.
Remember that we do not weight or scale the objectives…..yet.
Value of 1 - Row objective preferred over column objective
Value of 0 – Column objective preferred over row objective
Value of 0.5 – Objectives valued equally

## Slide 17: Now consider the Pairwise Comparison Chart (PCC) as an aid in prioritising the Objectives.

## Slide 18: PCC for the formula car
So our Objectives and associated Metrics for this example in order of importance are:
Safe (deceleration force in the event of accident, g)
Fast (lap time, s)
Reliable (distance between re-builds, km)
Frugal (fuel consumption, L/100km)
Objectives | Fast | Reliable | Economic | Safe | Score
Fast | - | 1 | 1 | 0 | 2
Reliable | 0 | - | 1 | 0 | 1
Economic | 0 | 0 | - | 0 | 0
Safe | 1 | 1 | 1 | - | 3

## Slide 19: 1.3 Identifying Constraints
These are the common constraints
Cost
Schedule
Government regulation
Weight
Dimension
From the Client, the constraints may:
Be hard or fixed (e.g. size).
Be soft or negotiable (these need to be established).
Define Limits (e.g. upper/lower bounds of a parameter).
Be quantitative (i.e. have a number attached).
Be qualitative (e.g. could be a taste or feel or look).

## Slide 20: Constraints versus Objectives?
Weight
Engine Size
Wheel size
Material
Dimensions
length
width
Fuel tank capacity

## Slide 21: 1.4 Revise the Client’s Problem Statement
Aim for a single sentence….or at least a single “paragraph”.
Try to keep it simple (minimum number of words).
It must be clear and explicit.
It must be sufficiently broad (so as not to overly constrain your potential solutions).
(Dym: Write it in terms of a function (or functions)  But we won’t look at Functions until Phase 2).

## Slide 22
“What people say, what people do, and
what they say they do are entirely different!”
“Customers don't know what they want until you show them”

## Slide 23: Having Defined the Problem, now Develop a Problem Statement
Example: A Client’s Report:
“In a hot and poor country, food perishes too quickly”.
A new Engineer’s original attempt at a Problem Statement:
“Design and build a machine that keeps food fresh and cold for under $100”.
What is wrong with this statement?
It’s too narrow and specific.

## Slide 24
“In a hot and poor country, food perishes too quickly”.
 “Design and build a machine that keeps food fresh and cold for under $100”.
Why does it have to be a machine?
Is cold necessary?
What do we mean by fresh?
How quick is quick?
Why $100?
“Design a system to preserve food for a long period of time.

## Slide 25: Examples of Problem Statements for Formula SAE
“Design and construct a racing car.”

## Slide 26: Examples of Problem Statements for Formula SAE
“Design and construct a racing car.”
Vague.
“Design and construct a racing car that meets specific client controls concerning speed and cost.”
Vague.
“Design and construct a vehicle for competition that accelerates as quickly as possible in any required direction. Performance must be maximised and cost minimised whilst adhering to the rules regarding size and safety.”
Longer but at least has reasonable breadth whilst ensuring that the rules are acknowledged.
….Think about incorporating the objectives

## Slide 27: Problem Definition  Problem Statement
Problem definition is the process by which you arrive at a concrete Problem Statement.
Be careful:
One person’s problem statement is another person’s conceptual design.
How do I write a Problem Statement?
Think! Use tools as need-be:
  Listing objectives and constraints (Dym, p.40).
  Statement – Restatement Method (Voland, p. 92).

## Slide 28
Dym’s four parts of Defining the Problem:
1.1 Clarify Objectives.
1.2 Establish Metrics for Objectives.
1.3 Identify Constraints.
1.4 Revise the Client’s Problem Statement.
Then…..
1.5 Identify the Functions and Requirements
 Articulate the Problem Definition in Engineering terms.
Leave this last step alone for a while.
For now, concentrate on understanding the problem.

## Slide 29: Read the instructions on Moodle carefully! Be prepared for the assessment in Week 4

## Slide 30: Project Bionic Hand - Announcements
Technical Stream Enrolment:
      Enrol by 10pm tonight on Moodle!
      Aim for a diversity within your team
Technical Streams begin on Thursday at 2pm
      Biomedical - Red Centre M032
      Mechanical – Chem Sci M17
      Electrical – Lecture room TBC (see Moodle)
Mentor Meeting
      Monday 4pm or Thursday 4pm this week. See allocation on Moodle
      Complete your Team Contract and up-load it to Moodle
      Next week – Problem Statement Activity
Next Monday be here for the Conceptual Design Lecture

## Slide 31: Project DELTA- Announcements
Technical Stream Enrolment:
      Enrol by 10pm tonight on Moodle!
      Aim for a diversity within your team
Technical Streams begin on Thursday at 2pm
      Mechanical – Chem Sci M17
      Electrical – Lecture room TBC (see Moodle)
Mentor Meeting
      Team 01-23: Monday 4pm-5pm
      Team 24-47: Thursday 4pm-5pm. See allocation on Moodle
      Next week – Problem Statement Activity
Next Monday be here for the Conceptual Design Lecture